## Slide 1: PULSATILE FLOW
Master Presentation

## Slide 2
Plunger
External Pressure
Water collected
centrifugal pump+ controller
pressure sensor
Flow sensor
3D- DIC
Air Bag
Silicone tube
Data Acquisition system

## Slide 3
Plunger
          silicone tube
Water collected
centrifugal pump+ controller
Water Tank
IN LAST PRESENTATION-

## Slide 4: Old picture of pump

## Slide 5: Head drawing
Material- aluminium
Tolerance - ±0.5mm

## Slide 6: SPECIFICATIONS
Inner diameter- 6mm
Outer diameter-8mm
Flow rate- 300ml/min
Reynolds number-416
Pulse frequency-10 pulse/min

## Slide 7
Plunger
External Pressure
Water collected
centrifugal pump+ controller
pressure sensor
Flow sensor
3D- DIC
Air Bag
Silicone tube
Data Acquisition system

## Slide 8
Calibration of instruments-
Pressure sensor, flow sensor were calibrated.
Data Acquisition System was made using Arduino UNO.
Arduino was coded using its ide to read and give command to sensors according to calibrated values.
Arduino UNO is 10bit ADC.
Flow sensor was calibrated using beaker.
Pressure sensor was calibrated using pressure gauge and ADC relation with voltage.

## Slide 9
Sensor Calibration Concept-
Since Arduino is 10bit ADC(Analog to Digital Converter)-
For Pressure sensor-
Relating ADC Value to Voltage-
By above equation verified our sensor values.
For 0-1023 ADC values relate the 0-0.5Mpa pressure.

## Slide 10
PRESSURE SENSOR AND FLOW SENSOR
Type | Analog Pressure Sensor
Sensor Type | piezoelectric sensor
Thread Size | G 1/4"
Pressure Range (MPa) | 0 – 0.5
Operating Voltage (VDC) | 5
Output Voltage (VDC) | 0.5 ~ 5
Error | 0.1% FS
Type | Digital Flow Sensor
Sensor Type | Hall effect sensor
Thread Size | G 1/4"
Flow Range (l/min) | 0 – 6
Operating Voltage (VDC) | 5
Output Voltage (VDC) | 0.5 ~ 4.5
Error | 2%

## Slide 11
Data Acquisition System
SOFTWARES USED FOR PROCESSING DATA AND CODING
ARDUINO IDE (Coding)
Chart: 
RESULTS-
CONNECTED TO PC

## Slide 12
Chart: Pulsatile flow waveform
Flow rate (ml/sec) = 3.18674 *sin (1.03332 *t +1.67248)+4.95948
FLOW WAVEFORM IN SETUP

## Slide 13
Equations-
Flow rate (ml/sec) = 3.18674 *sin (1.03332 *t +1.67248)+4.95948
Velocity (m/sec) = 0.112765 *sin (1.03332 *t +1.67248)+0.175494
Pipe inner diameter- 6mm
Pipe outer diameter- 8mm
Area- 2.826e-5
Chart: Velocity Profile

## Slide 14
Transparent Airbag was made-
The pressure that the bag can withstand =200mm Hg.
Airbag material thickness is 23 micron.
The Results taken are obtained by using complete elastic tube from start to end.
Acrylic box to enclose airbag incomplete.

## Slide 15
3D Digital Image Correlation-
Picture captured
PICTURES TRANSFERED TO PC
System Calibration
SOFTWARES USED FOR IMAGE PROCESSING
Results-
IMAGE PROCESSING

## Slide 16
DIC Calibration-
Use pattern whose parameters are known.
Rotate the pattern at different angle and capture pictures.
Give images to the system and try to get minimum error.